# Unit R113 – Electronic principles

# RC circuits

## Task 1 – Charging a capacitor in series with a resistor

Resistor-Capacitor (RC) circuits are commonly used to provide electrical time delays.

Your task is to perform an experiment to explore and understand how this can be achieved.

Working in groups, connect the power supply, resistor and capacitor as shown in the circuit diagram.  Do not switch on the power supply yet – your teacher will need to check the circuit first!

You will need a voltmeter (or multimeter) to measure the voltage across the capacitor, and a stopwatch to do this at 10 second intervals.

Switch on the power supply and record voltage readings every 10 seconds up until 300 seconds

(5 minutes).  Tabulate your results in a table as shown below.

| Time | Voltage across capacitor (volts) |
| --- | --- |
| 0 | 0 |
| 10 |  |
| 20 |  |
| 30 |  |
| 50 |  |
| 100 |  |
| 300 |  |

Once you have completed the table, plot your results using either graph paper or Microsoft Excel – a simple x-y graph of voltage (y-axis) and time (x-axis) with the points joined up will do.  Remember to start a time=0 seconds with 0 volts across the capacitor.

- What do you notice about the shape of the graph?

- What is the time constant for the circuit (given by C x R)?

- How does the time for the capacitor to fully charge (to approximately 9v) relate to the time constant C x R?

## Task 2 – Effects of varying the value of C in the circuit

You are going to repeat the experiment from Task 1 using a higher-value capacitor.

Once your circuit has been checked by your teacher, switch on the power supply and record voltage readings every 10 seconds up until 300 seconds (5 minutes).  Tabulate your results as last time in a table as shown on the next page.

| Time | Voltage across capacitor (volts) |
| --- | --- |
| 0 | 0 |
| 10 |  |
| 20 |  |
| 30 |  |
| 50 |  |
| 100 |  |
| 300 |  |

Plot your results as before.

- What do you notice about the shape of the graph this time – how has it changed from that plotted in Task 1?

- What has been the effect on the circuit time constant by making the value of C bigger?

- Does the capacitor charge fully (to approximately 9v) in 300 seconds – and if not how long will it take?

- If the value of the capacitor cannot be changed, what is another way of changing the circuit time constant?

# Text boxes

d.c.Voltage Source

9 V

470k(

Vc

100µF

d.c.Voltage Source

9 V

470k(

Vc

100µF

OCR Resources: the small print
OCR’s resources are provided to support the teaching of OCR specifications, but in no way constitute an endorsed teaching method that is required by the Board, and the decision to use them lies with the individual teacher.   Whilst every effort is made to ensure the accuracy of the content, OCR cannot be held responsible for any errors or omissions within these resources. 
© OCR 2014 - This resource may be freely copied and distributed, as long as the OCR logo and this message remain intact and OCR is acknowledged as the originator of this work.

OCR acknowledges the use of the following content: Maths and English icons: Air0ne/Shutterstock.com, satellite: puchan/Shutterstock.com,

shoes: Natali Glado/Shutterstock.com, mp3 player: You can more//Shutterstock.com, Tennis racket: ID1974/Shutterstock.com, Washing machine:

KKulikov/Shutterstock.com, London eye: 1000 words/Shutterstock.com, Sports car: GuoZhongHua/Shutterstock.com,

Bread: v.s.anandhakrishna/Shutterstock.com,