# Transition Guide – Physics in Action

# Making a light meter activity

Collect the following equipment:

LDR

resistor

voltmeter

battery

wires

Set up this circuit:

Check that the voltmeter reading changes when you cover the LDR with your hand.

Go around and record the voltmeter reading in different places in the table below:

| Location | Voltmeter reading / V |
| --- | --- |

How does the light level affect the voltmeter reading?

What could this device be used for? E.g. in sport.

# Text boxes

R

V

OCR Resources: the small print
OCR’s resources are provided to support the teaching of OCR specifications, but in no way constitute an endorsed teaching method that is required by the Board, and the decision to use them lies with the individual teacher.   Whilst every effort is made to ensure the accuracy of the content, OCR cannot be held responsible for any errors or omissions within these resources. 
© OCR 2016 - This resource may be freely copied and distributed, as long as the OCR logo and this message remain intact and OCR is acknowledged as the originator of this work.

OCR acknowledges the use of the following content: n/a

Please get in touch if you want to discuss the accessibility of resources we offer to support delivery of our qualifications: resources.feedback@ocr.org.uk

We’d like to know your view on the resources we produce.  By clicking on ‘Like’ or ‘Dislike’ you can help us to ensure that our resources work for you.  When the email template pops up please add additional comments if you wish and then just click ‘Send’.  Thank you.

If you do not currently offer this OCR qualification but would like to do so, please complete the Expression of Interest Form which can be found here: www.ocr.org.uk/expression-of-interest